1. DHCP messages sent over UDP.

2.

-Discover: Source Port: 68 Destination Port: 67
-Offer: Source Port: 67 Destination Port: 68
-Request: Source Port: 68 Destination Port: 67
-ACK: Source Port: 67 Destination Port: 68
-The port numbers is the same as in the example given in this lab assignment.

3. The link-layer (e.g., Ethernet) address of my host.

4. What values in the DHCP discover message differentiate this message from the DHCP request message?
DHCP Message Type.

5. The value of the Transaction-ID in each of the first four (Discover/Offer/Request/ACK) DHCP messages? 0x3e5e0ce3, 0x3e5e0ce3, 0x3e5e0ce3, 0x3e5e0ce3.
What are the values of the Transaction-ID in the second set (Request/ACK) set of DHCP messages?
0x3e5e0ce3, 0x3e5e0ce3
What is the purpose of the Transaction-ID field?
Server identify different request of client.

6.
Discover source 0.0.0.0 Destination 255.255.255.255
Offer source 192.168.1.1 Destination 255.255.255.255
Request source 0.0.0.0 Destination 255.255.255.255
Ack DHCP 192.168.1.1 Destination 255.255.255.255

7. The IP address of your DHCP server: 192.168.1.1

8. What IP address is the DHCP server offering to your host in the DHCP Offer
message? Indicate which DHCP message contains the offered DHCP address.
192.168.1.1
Option: (t=53,l=1) DHCP Message Type = DHCP Offer
The length of DHCP Message type is 1 and the DHCP offer is (2)

9. Relay agent IP address: 0.0.0.0. There is no relay agent in my experiment.

10. The subnet mask line tells the client which subnet mask to use. The router line indicates where the client should send messages by default.

11. Requested IP Address: 192.168.1.101

12. The lease time is the amount of time the DHCP server assigns an IP addresses to a client.

13. The DHCP message cancels the IP address that is given to it by the server. The server does not send an achknowlegement. If the release message is dropped, then the server must wait until the lease time is up before that address can be used again.

14.  Yes, there are ARP packets. It make sure that the IP addresses are not already in use.